Privileged Instructions: Can only be executed by the OS, not available to user code
- ex: place value in control register,

Dual Mode operation:
- User Mode: Only user instructions
- Kernel mode: Full access

Interrupts:
- Separate device, such an i/o device communicating with cpu
- Sends hardware signal to get attention of cpu
- Could also be a timer that signals something is over
- Interrupts can occur at any time, device may send one after completing a task for example
- Added into the Fetch/ Execute cycle. Almost all the time they are enabled, but if not it will just fetch and execute
- Internal examples: Program exception (division by zero), program trap (control transfer instruction to request interrupt)
- Can be used intentionally in some software

Interrupt Processing:
- OS determines the nature of interrupt (often numbered)
- Save state of interrupted process (running program) so it can be resumed later if needed
- Some interrupts are completely unrelated to the current process

Saving process state:
- All the bit patterns related to the process
- Machine language in RAM
- data objects in RAM
- Register states
- PC – address where interrupt occurred
- PSW – status bits (including user/kernel mode)
- Any general register which are used by the OS to handle interrupt
- These need to be saved to RAM

Interrupt Processing cont:
- Acknowledges the interrupt
- Turn on kernel mode
- Saves PC and the PSW
- Places address of the ISR into the PC
* This starts ISR that will have its own save restore protocol
- Many processors have additional special microprocessors to handle interrupts faster

Interrupt Categories:
- Hardware: signal from device
- Software: signal from program currently executing
* Exception